Rev A 9/23/16 Lecture 4

Digital Information

- Number System

To convert another number system to decimal or base 10

  - Decimal mnpr10 = ……. ( mx103 ) + ( nx102 ) + ( px101  ) +  (r x 100  )

Digit members = 0, 1, 2, ………9

Counting Members = 0, 1, 2, ………9, 10, 11, …

Decimal Counting from Jason Schanker of Molloy college

http://www.youtube.com/watch?v=ESIJku1NWx4

  - Binary  mnpr2 = ……. ( mx23 ) + ( nx22 ) + ( px21  ) +  (r x 20  )

Digit members = 0, 1

Counting Members = 0, 1, 10, 11

Binary Counting from Dr. Michael Littman of Rutgers

http://www.youtube.com/watch?v=4p-9-nK-mwY&eurl=

  - Hex mnpr16 = ……. ( mx163 ) + ( nx162 ) + ( px161  ) +  (r x 160  )

Digit Members = 0, 1, 2, ………9, A. B. C, D, E, F

Counting Members = 0, 1, 2, ………9, A. B. C, D, E, F, 10, 11, …

  - Quad mnpr4 = ……. ( mx43 ) + ( nx42 ) + ( px41  ) +  (r x 40  )

Digit Members = 0, 1, 2, 3

Counting Members = 0, 1, 2, 3, 10, 11, 12, 13, 100, 101, …

  - Other base (e.g.base 8)  mnpr8 = ……. ( mx83 ) + ( nx82 ) + ( px81  ) +  (r x 80  )

Counting Members = 0, 1, 2, ………,7

Counting Members = 0, 1, 2, ………,7, 10, 11

To convert binary to hex combine in 4 bit groups starting from the least significant bit (lsb, rightmost bit)

Binary  Hex  		Binary  Hex

00002 = 016	 	10002 = 816

00012 = 116		10012 = 916

00102 = 216		10102 = A16

00112 = 316		10112 = B16

01002 = 416		11002 = C16

01012 = 516		11012 = D16

01102 = 616		11102 = E16

01112 = 716		11112 = F16

To convert binary to quad combine in 2 bit groups starting from the least significant bit (lsb, rightmost bit)

002  =  04

012  =  14

022  =  24

032  =  34

To convert decimal to binary see “Fluency” 3rd edition pages 282 to 283

Example 7910 = ?2

| Number | 79 | 79 | 15 | 15 | 15 | 7 | 3 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Place value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |
| Subtract |  | 15 |  |  | 7 | 3 | 1 | 0 |
| Binary | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 |

7910 = 10011112

EXERCISES

- 100112 = _______10

- 1001102 = _______ 10

- What number in decimal is 100 times 4510 = _______10

- What number in binary is 4 times 10110012 = ______2

- 1010112 = _______16 = _______10 = _______4

- A4E16 = _______2

- 3214 = ________2

- Character representation

In digital we need to represent characters in a binary mode (1’s and 0’s)

Upper case alphabet = 26

Lower case alphabet = 26

Numbers = 10

Total =62 + a number of other characters to be used in text such as (space, ., ,, %, $,…….)

Therefore minimum amount required = 128 or 7 bits

Ascii code used which is a 7 bit representation

Extended Ascii code which is an 8 bit representation

Ascii Reference http://www.cdrummond.qc.ca/cegep/informat/Professeurs/Alain/files/ascii.htm

Table ASCII -I

TABLE ASCII -II

To obtain the asci character from decimal value just hold down the alt key while at the same time keying in the decimal value using the pc number pad.

Using the number pad determine the asci characters below

09810 = _______ ascii character

23610 = _______ ascii character

DIGITAL APPLICATION

Proposed DNA (nucleotides(nt)) code for storage

By

Alfonso Jiménez-Sánchez

http://internationalinventjournals.org/journals/IIJBB/archive/2013/October_vol-1-issue-1/fulltext/Jimenez-Sanchez.pdf

Future biological storage systems will be able to store large digital information using very small volume

Base 4 numbering system

0004=010=AAAnt

0014=110=AATnt

0024=210=AACnt

0034=310=AAGnt

0104=410=ATAnt

0114=510=ATTnt

0124=610=ATCnt

0134=710=ATGnt

1004=810=ACAnt

4 Base 4 nt symbols ATCG should cover the full 256 ascii characters

ACATnt = _______4 = _________ 10 = _______ asci character