Lecture 5

Internet. Lan, and Domains

- Introduction

  - Problem

Old computer systems consisted of a major main frame attached to many terminals.   Upon the introduction of the pcs the problem of resource sharing such as files, printing, and communication became evident.

  - Solution

Tie together computers so they can share hardware and software  resources.  Connection between a multitude of computers set up as a local area network (Lan – Same network tied together in a small geographical area such as a floor or building), wide area network (Wan – Same network connected together through a large geographical area such as throughout a country or many countries), internetworking  (internet – A multitude of networks connected through communication links together).

  - History

    - Arpanet (Advanced Research Projects Agency) started in 1969 by DOD.  Tied four sites into one network, UCLA, University of California at Santa Barbara, Stanford Research Institute, and the University of Utah.

    - Internet proposed by Vint Cerf and Bob Kahn, members  of Arpanet,   First implementation in October 1977 consisting of the three networks Arpanet, packet radio, and packet satellite.

- Communication Layers

Application

Presentation

Session

Transport

Network

Data Link

Physical

- Physical - It defines the electrical and mechanical specs of the interface and the transmission media so as to transmit and receive the digital bits.

- Data Link - Ensure the accurate transmission of data from two linked systems.

- Network - Transmission of data from a device on one network to a device on another network.

- Transport – Sees to error free transmission of data from end to end devices on different networks.  Segments or puts back together pieces of the message coming from or going to the transmission links.

- Session – sets up a dialog between the two communicating software

- Presentation – Allows for the understanding of info between the two package.  Deals with such areas as encoding, encryption, and compression.

- Application – Allows the user to access the network.

Internet. Lan, and Domains (continued)

C. Lan - Ethernet Network (Logical Bus Topology)

A

`

Any system can contend for the line and talk with any other system

Each device talks at the data link level 2.  Each system gets a network interface card called a NIC which is has a physical address (48 bits or 6 bytes) defined in hex as XX-XX-XX-XX-XX-XX burned into it and called the MAC address.  This way any device can send info to another unit on the network by addressing it.  All other units seeing it’s not for them will ignore the info.  Each piece of info sent is called a frame.

Frame

| Preamble | SFD | DA | SA | Type | Data | CRC |
| --- | --- | --- | --- | --- | --- | --- |
| 7 bytes | 1 byte | 6 bytes | 6 bytes | 2 bytes | 46-1500 bytes | 4 bytes |

SFD is start frame delimiter

DA is destination address

SA is source address

Type indicates type of data in the frame

CRC is cyclic redundancy check used for error checking

MAC address – OUI is the first 3 bytes registered with the IEEE organization.

http://standards.ieee.org/regauth/oui/index.shtml)

MAC address format

http://en.wikipedia.org/wiki/MAC_address

Internet. Lan, and Domains (continued)

Can ascertain MAC address of your network and wireless card through use of the following utilities.

Command window ipconfig /all or

Sys info>components>network>adapter

Destination MAC address of FF- FF- FF – FF – FF – FF is called a broadcast address which will be read by all systems on the network of the device transmitting the frame.

MAC addresses are to be registered and unique.  To secure systems especially in wireless networks the use of MAC filtering is adopted.

Physical device

Tying together the systems to one network is a piece of equipment called a hub.

Speed

10 base T 10 megabits / sec with a UTP cable and RJ45 connector

fast Ethernet 100 megabits / sec with a UTP cable and RJ45 connector

10 base T UTP 8 pin wiring

| pins | Strand colors | name |
| --- | --- | --- |
| 1 | white and orange | TX+ |
| 2 | orange | TX- |
| 3 | white and green | RX+ |
| 4 | NC | * |
| 5 | NC | * |
| 6 | green | RX- |
| 7 | NC | * |
| 8 | NC | * |

Internet. Lan, and Domains (continued)

100 base T UTP 8 pin wiring

| 1 | white and orange | TX_D1+ |
| --- | --- | --- |
| 2 | orange | TX_D1- |
| 3 | white and green | RX_D2+ |
| 4 | blue | BI_D3+ ** |
| 5 | white and blue | BI_D3- ** |
| 6 | green | RX_D2- |
| 7 | white and brown | BI_D4+ ** |
| 8 | brown | BI_D4- ** |

D Internet

Connecting Device

n

To the rest of the Internet

Internet. Lan, and Domains (continued)

We now need a logical address that transcends the network and allows communication from computer systems on separate networks.   A unique registered decimal address of 4 digits called the IP address is used.   An IP address is assigned to the system’s network  card depending on the connection to the network unlike the MAC address which is independent of location.

Example IP address format 156.34.27.5

Can ascertain IP address with the command window utility, ipconfig /all.

IP or internet address format

| Network ID | Host ID |
| --- | --- |

Networks are set up as follows

| Class A | 0. Net ID | 0.0.0 Host ID | To | 127. Net ID | 255.255.255 Host ID |
| --- | --- | --- | --- | --- | --- |

| Class B | 128.0. Net ID | 0.0 Host ID | To | 191.255. Net ID | 255.255 Host ID |
| --- | --- | --- | --- | --- | --- |

| Class C | 192.0.0. Net ID | 0 Host ID | To | 223.255.255 Net ID | 255 Host ID |
| --- | --- | --- | --- | --- | --- |

Also

Class A first bit is 0

Class B first and second bit are 10

Class C first, second and third bits are 110

The network IP address is defined with a host ID of zeroes

| Specific Addresses | Net ID | Host ID | Source or Destination |
| --- | --- | --- | --- |
| Network Address | Specific | All 0s | None |
| Direct broadcast address | Specific | All 1s | Destination |
| Limited broadcast address | All 1s | All 1s | Destination |
| This host on this network | All 0s | All 0s | Source |
| Specific host on this network | All 0s | Specific | Destination |
| Loopback address | 127 | Any (usually 0.0.1) | Destination |

Internet. Lan, and Domains (continued)

Many times we have networks that have what we call not real IP addressees.  The IP addresses have to be unique or there will be a problem in deciding who is to be delivered to.   Internally in some networks there are a range of IP addresses set aside to be used in this manner.  Externally from the outside world their gateway or router will have a valid unique address.  This is done sometimes because of the limited amount of IP numbers available.

Set aside “private IP addresses”

| Class A | 10.0.0.0 | To | 10.255.255.255 |
| --- | --- | --- | --- |
| Class B | 172.16.0.0 | To | 172.31.255.255 |
| Class C | 192.168.0.0 | To | 192.168.255.255 |

When a system has to send a frame to another on the network it may know the IP address, but not its physical address (MAC).  It uses a communication protocol called the address resolution protocol (ARP).  It sends out an ARP request with the known IP address that is broadcast to all systems. Only the host with the requested IP address then does an ARP reply with its corresponding MAC address.  This way a routing table is built up which binds the IP address with the MAC address.

Utility to see routing table

In command window arp –a

One such device we always note on the routing table is a gateway which is sometimes used interchangeably with a router.  In realty a gateway allows a connection between unlike networks while arouter is for similar ones only.

E. Software address

With the physical MAC address and the IP address we are able to reach the destination host, but that is not enough.  Each computer has many software programs.  There is a client program which tries to reach the server program.  The destination computer needs to know which program is being addressed.  This brings out the third required address to be used called the port address.  Some port addresses are standard for required functions such as a web server.  To see these one’s go to URL

http://www.iana.org/assignments/port-numbers

To find out info on the port addresses use the following utilities:

Command window

netstat

| Protocol | Local Address | Foreign Address | State |
| --- | --- | --- | --- |
| TCP | Computer name or IP address : port address | Computer name or IP address : port address | ESTABLISHED, TIME_WAIT, ….. |

Internet. Lan, and Domains (continued)

State tells the condition of the connection at the specific time.  Usually the condition is such that we make the connection with the server and then there is a closing of the port.  Sometimes a software program on the server and we do have in our own machines internal ones, will wait for connections and will be in a listening state.  This listening state has to have good security since it is a permanent open port condition.  It is like keeping your door open all the time.

To see all ports so that the listening ones are included use utility

Command windows netstat –a

Other options of the netstat utility are

Command window netstat –n provides information in IP terms only rather than computer name

Command window netstat –e provides historical statistics of traffic to the computer

| Parameter | Received | Sent |
| --- | --- | --- |
| Unicast packets |  |  |
| Non-unicast packets |  |  |
| Discards |  |  |
| Errors |  |  |

# Text boxes

A

C

B

Network A

Network B

Network C

Router

Router